## Slide 1
Digital Key Roadmap
One product family. Two protocol routes. Three delivery options.
1 / 3
01 Current Demo | 02 Vehicle Engineering | 03 Full Product | 04 Production Delivery
Non-CCC protocol BTCS ranging and positioning validation | Layout and calibration Phone integration Reliability and security Power consumption | Activation, authentication Permissions and sharing Revocation and control Cloud and factory tools Aftersales tools | Vehicle adaptation Ecosystem integration Certification and acceptance Production deployment
Three Product Delivery Options
Non-CCC Digital Key | CCC Digital Key | Combined Digital Key
Proprietary protocol Digital keys through the OEM app | CCC protocol Supported wallet integration | App and wallet support Unified experience and management
Both routes develop in parallel, with standalone or combined delivery.
Notes: Digital Key Roadmap
One product family, two protocol routes and three delivery options.
Development stages: current BTCS positioning demo, vehicle engineering, full product development, and production delivery.
The current demo validates BTCS ranging and positioning under a non-CCC protocol.
Vehicle engineering covers node placement, algorithm calibration, phone integration, positioning performance, reliability, power consumption and security validation.
Full product development covers key activation, identity authentication, permissions, sharing and revocation, vehicle control, cloud management, and factory and aftersales tools.
Non-CCC and CCC are parallel protocol routes. Each can form a complete standalone product, or both can form a combined product. Combined delivery provides unified experience and management while meeting each route's protocol, credential, security and ecosystem requirements. Select the radio configuration according to the vehicle, device support, desired experience and cost requirements.

## Slide 2
Vehicle Configuration and Total Cost
Positioning targets drive hardware choices. Compare cost for the same requirements.
2 / 3
Configuration | Experience / Target | Cost Baseline / Additions | Selection Criteria
NFC + BLE Basic access | Tap to unlock / start App vehicle controls Vehicle status | NFC reader, BLE module Security components Vehicle integration | Basic access Precise positioning / passive access need added design and validation
NFC + BLE-CS BTCS positioning | Distance sensing Approach detection Zone detection (subject to validation) | CS chips, nodes, antennas Wiring, calibration, tests Potential UWB removal Cost follows final design | One node: distance input Zones: more nodes or other inputs Verify foreground, background and locked-screen support
NFC + BLE + UWB | Secure ranging Positioning Passive entry / start where supported | UWB chips and antennas Anchors and calibration Ecosystem integration and testing | Nodes: coverage / redundancy BTCS may assist wake-up where supported Verify phone / ecosystem support
Confirm target zones, node layout and phone behavior in foreground, background and lock screen.
Cost scope: full vehicle BOM, software integration, calibration, certification and testing.
Protocol and hardware are separate choices. CCC can use NFC + BLE. WCC3 passive entry / start requires UWB.
Notes: Vehicle Configuration and Total Cost
Positioning targets determine the hardware configuration. Compare complete vehicle costs against the same requirements.
NFC + BLE provides tap-based unlocking and starting, app vehicle controls and status queries. The cost baseline includes the NFC reader, BLE module, security components and vehicle integration. Precise positioning and passive access require additional design and validation.
NFC + BLE-CS targets distance sensing, approach detection and validated zone detection. One BLE-CS node provides a distance input. Inside/outside, door and trunk zone decisions require suitable node placement, multiple nodes or other position inputs. Cost additions include CS-capable chips, node and antenna counts, wiring, algorithm calibration and vehicle tests. A configuration may omit dedicated UWB radio hardware, but any vehicle cost advantage depends on the final design.
NFC + BLE + UWB targets secure ranging, position decisions and passive entry/start supported by the relevant ecosystem. Cost additions include UWB devices, antennas or anchors, placement and calibration, ecosystem integration and testing. Coverage, positioning needs and redundancy determine the node count. BTCS may assist approach detection and wake-up when supported.
Confirm the intended experience, phone coverage, foreground/background/locked-screen operation and complete vehicle cost. CCC can use the NFC + BLE WCC2 configuration. WCC3 passive entry/start retains the UWB requirement. Node count, phone coverage and cost advantages require project validation and BOM calculation.
Sources:
Bluetooth SIG, Channel Sounding Technology Overview: https://www.bluetooth.com/channel-sounding-tech-overview/
Bluetooth SIG, Channel Sounding and UWB cooperation and cost factors: https://www.bluetooth.com/blog/bluetooth-channel-sounding-will-expand-the-market-presence-of-distance-awareness/
CCC Digital Key certification scope: https://carconnectivity.org/digital-key/ccc-digital-key-certification/
CCC-TS-101 Digital Key v4.1.0, physical pages 436, 476, 561, 562 and 565.
Local product definition: docs/product/digital-carkey-product-definition.md, WCC1/WCC2/WCC3 capability combinations.

## Slide 3
BTCS Across Non-CCC and CCC Routes
The current demo validates non-CCC positioning. BTCS can also operate within CCC.
3 / 3
Non-CCC Route
Provides ranging and positioning for the selected configuration.
Node placement and algorithms support distance, zone and approach detection.
CCC Route
CCC 4.1 includes optional BTCS support.
Both phone and vehicle must support BTCS and the required protocol flow.
BTCS can assist approach-intent detection and system wake-up.
Combined Delivery
Combine radios for the access path, device support and vehicle configuration.
NFC, BLE, BTCS and UWB support app and wallet experiences.
Vehicle actions depend on valid key permissions, security policies and position conditions.
Acceptance: phone coverage, operating scenarios, zone accuracy, latency, false triggers and fallbacks.
WCC3 retains UWB secure ranging and positioning requirements. Phone coverage, security, power and cost need validation.
Notes: BTCS Across Non-CCC and CCC Routes
BTCS can serve both non-CCC and CCC digital key routes.
Non-CCC route: BTCS provides ranging and positioning for the selected configuration. Vehicle node placement and algorithms support distance, zone and approach detection.
CCC route: CCC 4.1 includes optional BTCS support. Both phone and vehicle must support the capability and implement the required protocol flow. BTCS can assist approach-intent detection and system wake-up within a CCC digital key connection.
Combined delivery: combine NFC, BLE, BTCS and UWB according to the access path, device support and vehicle configuration to provide app and wallet digital key experiences.
Experience targets include approach detection, vehicle wake-up and location-dependent vehicle functions. Vehicle actions depend on valid key permissions, security policies and position conditions. Evaluate total vehicle cost while meeting the experience, security and device coverage requirements.
Product acceptance requires a compatible phone list, operating scenarios, zone accuracy, response latency, false-trigger rate, fallback behavior and agreed acceptance criteria. BTCS is optional in CCC. WCC3 passive entry retains UWB secure ranging and positioning requirements. The current demo validates non-CCC BTCS positioning. Complete product coverage, vehicle security, power and cost performance still require validation.
Sources:
CCC-TS-101 Digital Key v4.1.0, physical pages 436, 476, 561, 562 and 565.
Bluetooth SIG: https://www.bluetooth.com/channel-sounding-tech-overview/
CCC certification scope: https://carconnectivity.org/digital-key/ccc-digital-key-certification/